## Slide 1
SNPP Ocean SIPS
status
SNPP Applications Workshop
18 November 2014
Bryan Franz
and the
Ocean Biology
Processing Group

## Slide 2: VIIRS Ocean Product Status
Currently producing and distributing ocean color products
  near real-time and refined (15-45 days later for updated ancillary)
  Level-1A & Level-2 (granule), and Level-3 (global) products
  MODIS continuity algorithms
Recently updated forward-stream production and completed full mission ocean color reprocessing (R2014.0):
  significantly improved instrument calibration
  full suite of ocean products consistent with MODIS
  new CF-compliant netCDF4 file format for L2 & L3
B. Franz, 17 Nov 2014

## Slide 3: Generating Full Set of Ocean Color Products using MODIS Continuity Algorithms
Level-2:
  OC suite: Rrs(l), Chl, Kd(490), PIC, POC, PAR, AOT, Angstrom
  IOP suite: a(l), bb(l), aph(443), adg(443), bbp(443), uncertainties
  VIIRS l = 410, 443, 486, 551, 671
  MODIS l = 412, 443, 469, 488, 531, 547, 555, 645, 667, 678
  total of 31 individual Level-2 products in two files per granule
Level-3:
daily, 8-day, monthly, seasonal, and annual global binned composites
4.6 and 9.2 km mapped products
B. Franz, 17 Nov 2014
Notes: full set of products proposed by me and others on the VIIRS ST (mostly already implemented in context of PEATE)
biggest limitation for VIIRS is spectral bands

## Slide 4: VIIRS & MODISA Winter 2012 NASA/OBPG Calibration & Processing
VIIRS
VIIRS
MODISA
MODISA
Chlorophyll
Kd(490) Diffuse Attenuation
MODISA
VIIRS
B. Franz, 17 Nov 2014

## Slide 5: R2014.0 Instrument Calibration
Significantly improved instrument calibration developed for ocean color through the NPP Ocean Science Team (PI Franz, Eplee et al. in prep).
Based on solar calibration, corrected with lunar calibration.
Incorporating significant advancements in solar and lunar calibrator knowledge (solar unit vector fix, lunar libration corrections, etc.).
implemented as a continuous calibration model that allows for extrapolation into the future (improved NRT calibration quality).
Including corrections to the detector relative calibration to reduce image striping artifacts.
B. Franz, 17 Nov 2014
Notes: lunar-based
exponential model allows forward-stream extrapolation
destriping

## Slide 6: Reduced Image Striping
Revised instrument calibration includes detector relative calibration to reduce image striping artifacts.
Version R2013.2
Version R2014.0
B. Franz, 17 Nov 2014

## Slide 7: Climate Application: Chlorophyll Anomaly Record
PSO Anomaly
SeaWiFS
MODISA
NASA VIIRS
MERIS
Multivariate Enso Index (MEI)
PSO
Permanently Stratified
Ocean (PSO)
mean SST > 15C
Following Franz, B.A., D.A. Siegel, M.J. Behrenfeld, P.J. Werdell (2013). Global ocean phytoplankton [in State of the Climate in 2012]. Bulletin of the American Meteorological Society, 94(8), S75-S78.

## Slide 8: Data Latency
L1 & L2 products typically available within 3-5 hours from time of observation
3 hrs
5 hrs
2014
B. Franz, 17 Nov 2014

## Slide 9: Data Access
http://oceancolor.gsfc.nasa.gov/cms/dataaccess
Supporting
  Level-1 and Level-2 scene browse for direct access and bulk order
  Level-3 browse and direct access
  direct access archive (suitable for scripted bulk download)
  subscription service
also
  coincident field data access
  validation match-up analyses (primarily AERONET-OC Rrs validation)
B. Franz, 17 Nov 2014

## Slide 10: OBPG Multi-mission Level 1/2 Browser showing VIIRS full mission
B. Franz, 17 Nov 2014

## Slide 11: OBPG Level 3 Browser
B. Franz, 17 Nov 2014

## Slide 12: SeaDAS Open Source Software for Application Development
Display & analysis for VIIRS
  SDRs
  EDRs
  NASA L2
  NASA L3
Processing capability
  Level 1A to Level 2
  Level 2 to Level 3
  Alternative algorithms
Processing source code
  Application development
B. Franz, 17 Nov 2014

## Slide 13: Future Plans
Add SST production (Spring 2015)
  MODIS heritage algorithm
  support for GHRSST
Transition from NOAA RDR and IDPS processing code to NASA Level-0 to Level-1B process and formatting (Spring 2015)
  Level-0 via EDOS (may reduce latency further)
  Level-1A produced in ~5 minute granule size (no more 86-sec granules!)
  Level-1A, Level-1B, and geolocation in compressed netCDF4 format
  fully independent instrument calibration approach
B. Franz, 17 Nov 2014

## Slide 14: References
data access:
http://oceancolor.gsfc.nasa.gov/cms/dataaccess/
file format:
http://oceancolor.gsfc.nasa.gov/cms/format/l2nc_viirs.html
processing history:
http://oceancolor.gsfc.nasa.gov/cms/reprocessing/
algorithm descriptions:
http://oceancolor.gsfc.nasa.gov/cms/atbd/
B. Franz, 17 Nov 2014

## Slide 15: back-up

## Slide 16
VIIRS Level-1A to NASA Level-2 and Level-3
L2GEN
Level-1 to Level-2
(common algorithms)
SeaWiFS L1A
MODISA L1B
MODIST L1B
OCTS L1A
MOS L1B
OSMI L1A
CZCS L1A
MERIS L1B
OCM-1 L1B
OCM-2 L1B
VIIRS L1A
GOCI L1B
L8 OLI L1T
Level-2 to Level-3
Level-2 Scene
observed
radiances
ancillary data
water-leaving
reflectances &
derived prods
Level-3 Global
Product
vicarious calibration
gain factors
predicted
at-sensor
radiances
in situ water-leaving
radiances (MOBY)
sensor-specific tables:
Rayleigh, aerosol, etc.

## Slide 17: Instrument Temporal Calibration
> 35% sensitivity loss in NIR band M7 (862), but stabilized.

## Slide 18: Direct Access Archive

## Slide 19: Data Latency
L1 & L2 products typically available within 3-5 hours from time of observation