## Slide 1
Using VIIRS DNB
and
OMI NO2 retrievals
for
constraining NOx Emissions
Brad Pierce
NOAA/NESDIS
Second Suomi NPP Applications Workshop November 18-20, 2014, Huntsville, Alabama

## Slide 2
Background: National Trends in Nitrogen Dioxide (NO2) Levels
Russell et al., ACP 12, 12197-12209, doi:10.5194/acp-12-12197-2012, 2012.
Overall, surface and column NO2 amounts are declining over the US due to regulations from the Clean Air Act
OMI Berkeley High-Resolution (BEHR) NO2 Column Retrievals
EPA NO2 trends from ground monitoring
http://www.epa.gov/airtrends/nitrogen.html
32±7% reduction 2005-2011

## Slide 3
Background: The US EPA 2011 National Emissions Inventory
http://www.epa.gov/ttn/chief/net/2011inventory.html
The National Emissions Inventory (NEI) is a comprehensive and detailed estimate of emissions of air pollutants from all air emissions sources.
NEI is used to constrain Air Quality modeling in support of State Implementation Planning (SIP) required by the EPA

## Slide 4
On-road Cars and Trucks are the major source of NO2 emissions
Background: The US EPA 2011 National Emissions Inventory

## Slide 5
Power Plants are another major source of NO2 emissions
Background: The US EPA 2011 National Emissions Inventory

## Slide 6
Background: The US EPA 2011 National Emissions Inventory
Oil and Gas Production is another major source of NO2 emissions

## Slide 7
U.S Energy Information Administration (http://www.eia.gov/)
Background: National Trends in Oil and Gas Production
Oil and Gas Production has risen significantly since 2011

## Slide 8
Oil and Gas Production activities can be monitored with the Visible Infrared Imaging Radiometer Suite (VIIRS) Day-Night-Band (DNB) imagery
VIIRS DNB Composite Imagery from NOAA National Geophysical data Center
Question:
Can we use VIIRS DNB and OMI NO2 retrievals for constraining NOx Emissions?

## Slide 9
Approach
Evaluate the spatial correlation between NEI 2011 NOx emissions and VIIRS DNB on a regional scale
Evaluate the spatial correlation between NEI 2011 NOx emissions and OMI NO2 columns on a regional scale
Use VIIRS DNB radiances to generate a spatially enhanced OMI NO2 column retrieval appropriate for constraining Air Quality model emissions through Data Assimilation

## Slide 10
NEI 2011 total NO emissions inventory
(4km all area+point sources)
Provided by Stu McKeen (NOAA/ESRL)

## Slide 11
NEI 2011 total NO emissions inventory
(4km all area+point sources)
Provided by Stu McKeen (NOAA/ESRL)
Salt Lake City
Phoenix
Denver
Background
Background
Background
Background
Background
Minneapolis
St. Louis
Atlanta

## Slide 12
NEI 2011 Oil&Gas NO emissions inventory
(4km all area+point sources)
Provided by Stu McKeen (NOAA/ESRL)
Permian
Barnett
Haynesville-Bossier
Woodford
Eagle Ford
New Albany
Floyd-Neal
Marcellus
Antrim
Uinta Basin
San Juan Basin
Denver-Julesburg Basin
Powder River Basin
Green River Basin
Piceance Basin
Williston Basin

## Slide 13
Investigate relationship NEI 2011 emissions and SNPP VIIRS Day Night Band (DNB) radiances (2012 cloud free composite, 15 arc second resolution) for specific urban and oil and gas regions
Conduct spatial analysis to determine geolocation
VIIRS DNB
SNPP VIIRS cloud-free composite (2012/4/18-26 and 2012/10/11-23) DNB data on 15 arc sec grid from Earth Observation Group, NOAA National Geophysical Data Center in GEOTIFF format
http://www.ngdc.noaa.gov/eog/viirs/download_viirs_ntl.html

## Slide 14
SNPP VIIRS 2012 cloud-free composite
(15 arc sec grid)
Earth Observation Group, NOAA National Geophysical Data Center

## Slide 15
Aggregated VIIRS DNB radiances vs NEI 2011 modeled/gridded NO emissions
Region Z: Atlanta

## Slide 16
NEI 2011 modeled/gridded NO emissions
Region Z: Atlanta

## Slide 17
Aggregated VIIRS DNB radiances
Region Z: Atlanta

## Slide 18
Aggregated VIIRS DNB radiances vs NEI 2011 modeled/gridded NO emissions
Region S: Eagle Ford

## Slide 19
NEI 2011 modeled/gridded NO emissions
Region S: Eagle Ford
Laredo, TX
I35

## Slide 20
Aggregated VIIRS DNB radiances
Region S: Eagle Ford
Laredo, TX
I35

## Slide 21
Aggregated VIIRS DNB radiances
Region S: Eagle Ford
Laredo, TX
I35

## Slide 22
Aggregated VIIRS DNB radiances
Region S: Eagle Ford
Laredo, TX
I35

## Slide 23
Aggregated VIIRS DNB radiances vs NEI 2011 modeled/gridded NO emissions
Region N: Williston Basin

## Slide 24
NEI 2011 modeled/gridded Total NO emissions
Region N: Williston Basin
Minot
Sidney
Williston

## Slide 25
2012 VIIRS DNB Radiances
Region N: Williston Basin
Minot
Sidney
Williston

## Slide 26
2012 VIIRS DNB Radiances
Region N: Williston Basin
Minot
Sidney
Williston

## Slide 27
2012 VIIRS DNB Radiances
Region N: Williston Basin (103W 48N 0.1o Zoom)

## Slide 28
Google Earth
Region N: Williston Basin (103W 48N 0.1o Zoom)

## Slide 29
1km
Google Earth Zoom
Region N: Williston Basin
2.5km

## Slide 30
Google Earth Zoom
Region N: Williston Basin

## Slide 31
Chart: 2011 NEI NO emissions and 2012 VIIRS DNB correlation
 | 0.611 | 0.638 | 0.122 | 0.459 | 0.466 | 0.281 | 0.198 | 0.548 | 0.631 | 0.159 | 0.003 | 0.129 | 0.096 | 0.039 | 0.308 | 0.506 | 0.297 | 0.2 | 0.715 | 0.234 | 0.379 | 0.166 | 0.186 | 0.265 | 0.209 | 0.178 | 0.25 | 0.509 | 0.407 | 0.392
Summary of Regional Correlations 2011
A B C D E F G H I J K L M N O P Q1 Q2 Q3 R S T U V1 V2 V3 W X Y Z
Region
A= Salt Lake City
B=Phoenix
C=Uinta Basin
D=Green River Basin
E=Piceance Basin
F=San Juan Basin
G=Powder River Basin
H=Denver/Denver-Julesburg Basin
I=NW Background
J=SW Background
K=Northern Background
L=SW Background
M=Eastern Background
N=Williston Basin
O=Permian
P=Barnett
Q1=Haynesville-Bossie S
Q2=Haynesville-Bossie C
Q3=Haynesville-Bossie N
R=Woodford
S=Eagle Ford
T=New Albany
U=Floyd-Neal
V1=Marcellus S
V2=Marcellus C
V3=Marcellus N
W=Antrim
X=Minneapolis
Y=St. Louis
Z=Atlanta
VIIRS DNB shows reasonable (0.3-0.7) correlations with aggregated 2011 NEI NO emissions for urban areas (Salt Lake City, Phoenix, Denver/ Denver-Julesburg Basin, Minneapolis, St. Louis, Atlanta) and some O&G regions (Green River, Piceance, Permian, Barnett, Haynesville-Bossie North, Eagle Ford)

## Slide 32
Chart: 2011 NEI NO emissions and OMI BEHR NO2 correlation
 | 0.375 | 0.343 | 0.169 | 0.038 | 0.194 | 0.249 | 0.138 | 0.316 | 0.04 | 0.06 | -0.01 | 0.02 | 0.02 | 0.01 | 0.11 | 0.236 | 0.06 | 0.11 | 0.04 | 0.11 | 0.07 | 0.13 | 0.17 | 0 | 0.15 | 0.22 | 0.07 | 0.2 | 0.16 | 0.21
Summary of Regional Correlations 2011
A= Salt Lake City
B=Phoenix
C=Uinta Basin
D=Green River Basin
E=Piceance Basin
F=San Juan Basin
G=Powder River Basin
H=Denver/Denver-Julesburg Basin
I=NW Background
J=SW Background
K=Northern Background
L=SW Background
M=Eastern Background
N=Williston Basin
O=Permian
P=Barnett
Q1=Haynesville-Bossie S
Q2=Haynesville-Bossie C
Q3=Haynesville-Bossie N
R=Woodford
S=Eagle Ford
T=New Albany
U=Floyd-Neal
V1=Marcellus S
V2=Marcellus C
V3=Marcellus N
W=Antrim
X=Minneapolis
Y=St. Louis
Z=Atlanta
OMI BEHR NO2 shows lower (0.3-0.4) correlations with aggregated 2011 NEI NO emissions for Western urban areas (Salt Lake City, Phoenix, Denver/ Denver-Julesburg Basin) only
A B C D E F G H I J K L M N O P Q1 Q2 Q3 R S T U V1 V2 V3 W X Y Z
Region

## Slide 33
Use VIIRS Day Night Band (DNB) radiances to add sub-pixel (~4x4km) variability to native (13x24km) OMI NO2 retrieval
Region H=Denver/Denver-Julesburg Basin
Native OMI pixel

## Slide 34
Sub-divide each OMI pixel into 4x8 subsectors
Use VIIRS Day Night Band (DNB) radiances to add sub-pixel (~4x4km) variability to native (13x24km) OMI NO2 retrieval
Region H=Denver/Denver-Julesburg Basin

## Slide 35
Compute mean DNB radiance for each 4x8 subsectors
Compute linear regression between pixel mean DNB radiance and OMI BEHR NO2 for each swath
Use linear regression to redistribute OMI NO2 over sub-pixels
Adjust mean of sub-pixel NO2 to original pixel NO2
Use VIIRS Day Night Band (DNB) radiances to add sub-pixel (~4x4km) variability to native (13x24km) OMI NO2 retrieval
Region H=Denver/Denver-Julesburg Basin

## Slide 36
Using VIIRS Day Night Band (DNB) radiances to add (~4x4km) sub-pixel variability to native (13x24km) OMI NO2 retrieval Region H: Denver/Denver-Julesburg on August 02, 2014

## Slide 37
Using VIIRS Day Night Band (DNB) radiances to add (~4x4km) sub-pixel variability to native (13x24km) OMI NO2 retrieval Region N: Bakken on July 03, 2014

## Slide 38
VIIRS DNB shows reasonable (0.3-0.7) correlations with aggregated 2011 NEI NO emissions for urban areas (Salt Lake City, Phoenix, Denver/ Denver-Julesburg Basin, Minneapolis, St. Louis, Atlanta) and some O&G regions (Green River, Piceance, Permian, Barnett, Haynesville-Bossie North, Eagle Ford)
OMI BEHR NO2 shows lower (0.3-0.4) correlations with aggregated 2011 NEI NO emissions for Western urban areas (Salt Lake City, Phoenix, Denver/ Denver-Julesburg Basin) only
Using VIIRS Day Night Band (DNB) radiances to add sub-pixel variability to native OMI NO2 retrieval adds realistic sub-pixel structure.
Summary

## Slide 39
Airborne insitu, Geostationary Trace gas and Aerosol Sensor Optimization (GEO-TASO, Jim Leitch, Ball Aerospace) and Airborne Compact Atmospheric Mapper (ACAM, Scott Janz, NASA/GSFC) will be used to validate the spatially enhanced OMI NO2 retrievals during CalNex, DISCOVER-AQ, FRAPPE, and SONGNEX field missions.
Assimilation experiments will be conducted to assess the impact of spatially enhanced OMI NO2 retrievals on air quality within urban and oil and gas basins within regional air quality modeling systems (WRF-Chem, CMAQ)
brad.pierce@noaa.gov
Acknowledgement:
Funding for this work was provided by the NASA Air Quality Applied Science Team 2013 Oil&Gas Tiger Team Project (Anne Thompson, Lead)
Future Directions

## Slide 40
Extra Slides

## Slide 41
Aggregated VIIRS DNB radiances vs NEI 2011 modeled/gridded NO emissions
Region O: Permian

## Slide 42
NEI 2011 modeled/gridded Total NO emissions
Region O: Permian
Lubbock, TX
Midland, TX
Odessa, TX

## Slide 43
Aggregated VIIRS DNB radiances
Region O: Permian
Lubbock, TX
Midland, TX
Odessa, TX

## Slide 44
Aggregated VIIRS DNB radiances
Region O: Permian

## Slide 45
Aggregated VIIRS DNB radiances
Region O: Permian

## Slide 46
Aggregated VIIRS DNB radiances vs NEI 2011 modeled/gridded NO emissions
Region V1: Southern Marcellus

## Slide 47
NEI 2011 modeled/gridded Total NO emissions
Region V1: Southern Marcellus
Pikeville KY

## Slide 48
Aggregated VIIRS DNB radiances
Region V1: Southern Marcellus
Pikeville KY

## Slide 49
Aggregated VIIRS DNB radiances
Region V1: Southern Marcellus
Mountain Top Removal
Pikeville KY

## Slide 50
Aggregated VIIRS DNB radiances
Region V1: Southern Marcellus
McDowell FCI
1,692 Inmates