## Slide 1: Developing Retrieval Algorithms for NH3 (and CO) from NPP CrIS Measurements
Karen Cady-Pereira1, Helen Worden2
1. Atmospheric and Environmental Research (AER)
2. NCAR/NESL/ACD
Also: Mark Shephard, Ming Luo, Daven Henze, Juliet Zhu, Kang Sun, Mark Zondlo, Armin Wisthaler, AmyJo Scarino, Chantelle Londsale, Matthew Alvarado, Robert Pinder, John Walker, Jesse Bash

## Slide 2: TES and CrIS instruments
Two TES observation modes:
Global Surveys: 26 hours long, return to starting point every 16 days
Special Observations: higher sampling density over shorter tracks
0.625 cm-1 resolution is key for accurate CO retrievals
 | TES | CrIS
Satellite | AURA | NPP
Launch | July 2004 | October 2011
Resolution | 0.06 cm-1 | 0.625 cm-1
Footprint | 5x8 km rectangle | 14 km diameter circle
Repeat cycle | Once every 16 days | Daily
Equatorial crossing | 1:30 am and 1:30 pm | 1:30 am and 1:30 pm
Noise in NH3 window | 0.09 – 0.12 K | 0.03 – 0.06 K

## Slide 3: Why CO?
Important role in atmospheric chemistry & climate
  Sources are incomplete combustion (both fires & fossil fuel) & hydrocarbon oxidation
  Primary sink is oxidation by OH
  Precursor to CO2 and tropospheric O3
  Indirect RF of 0.23 W/m2 for CO emissions (IPCC AR5)
Ideal tracer for pollution transport
  Lifetime is weeks to months, so CO is transported globally, but not evenly mixed (like longer lived species)
  Easy to measure elevated CO above background levels
Global direct emissions of CO (~half of atmos. CO)
  ~500-600 Tg/yr anthropogenic (relatively stable)
  ~300-600 Tg/yr biomass burning (large interannual variability)
O
C

## Slide 4: CO has a trend
N. Hemisphere
S. Hemisphere
Consistent with a continuation of 1991-2001 trend for
NH surface CO: -0.8%/year (Novelli et al., JGR, 2003)

## Slide 5: …and a seasonal cycle
AIRS bias also shown in
George et al., ACP 2009
0° to 60°N
0° to 60°S

## Slide 6: NH3 Sources
Bi-directional
Flux
AGRICULTURE
Animal waste (temperature dependent)
Fertilizer application
Industry
Fertilizer
Coal Mining
Power generation
Biomass burning
Automobiles (catalytic converters)
Large urban centers
  50% of NH3 in LA area

## Slide 7: NH3 in the atmosphere
Long-range import
Long-range export
PM2.5 Particles
NH3 + HNO3NH4NO3
2 NH3 + H2SO4(NH4)2SO4
Increase incidence of cardiovascular and respiratory diseases
Increase number of CCN
Affect cloud radiative properties
Climate change
SO2, NOX decreasing
but NH3 forecast to increase

## Slide 8: Better emissions with TES NH3
Largest changes western US and Mexico
Used GEOS-Chem adjoint with TES NH3 profiles, averaging kernels and error covariances to optimize model
Optimized GC shows better agreement with AMoN network measurements
Zhu et al., 2013, JGR

## Slide 9: NH3 Algorithm structure
From each FOR (9 FOVs):
Water vapor profiles
Temperature profiles
Surface temperature
Cloud od?
SIPS @SSEC
From each FOV:
Radiances
Noise
Determine a priori and constraints from BT test.
First guess emissivity from University of Wisconsin database.
Optimal estimation first step:
Surface temperature
Emissivity
Cloud od?
SIPS @JPL
(AER algorithms)
Optimal estimation second step:
NH3 profile
Error estimates
Averaging kernels

## Slide 10: CO Algorithm structure
From each FOR (9 FOVs):
Water vapor profiles
Temperature profiles
Surface temperature
Cloud od?
SIPS @SSEC
From each FOV:
Radiances
Noise
A priori and constraints from MOPITTv5 climatology
First guess emissivity from University of Wisconsin database.
Optimal estimation first step:
Surface temperature
Emissivity
Cloud od?
SIPS @JPL
(AER algorithms)
Optimal estimation second step:
CO profile
Error estimates
Averaging kernels

## Slide 11: NH3 signal from TES and CrIS
Simulated spectra and NH3 signal
18 ppbv at surface
Detectability is ~ 1 ppbv under ideal conditions
But thermal contrast also plays a role
TES
CrIS

## Slide 12: TES and CrIS Sensitivity to NH3
Both instruments most sensitive to NH3 between 950 and 600 mbar
TES is more sensitive to amounts lower in the atmosphere
1 piece of information or less: DOFS<1.0
Collapse all information to a single point: RVMR
  Easier to compare with in situ measurements, models and other instruments
TES
CrIS

## Slide 13: Monitoring NH3 is difficult
NH3 is highly reactive
 highly variable in space and time
NH3 from an Open path Quantum Cascade Laser (QCL) on a moving platform in the San Joaquin Valley during DISCOVER-AQ 2013.
Miller et al., AMT, 2014

## Slide 14: NH3 from aircraft
DISCOVER-AQ campaign in January 2013 in the San Joaquin Valley
January 30
PBL from airborne HSRL backscatter
NH3 from PTR and Picarro
January 21

## Slide 15: How TES compares
January 30
P3B aircraft @ 300 m: point measurement
TES maximum sensitivity between 1 and 2 km
  5x8 km footprint
RVMR
TES and aircraft NH3 are well correlated
January 21

## Slide 16: Satellite and surface NH3
QCL directly under TES transect in the San Joaquin Valley on January 28, 2013

## Slide 17: CrIS NH3 – June 11, 2013
SENEX area

## Slide 18: CrIS NH3 – June 2, 2014
Mid-Atlantic states

## Slide 19: Where is this?

## Slide 20: CrIS NH3 – June 13, 2012
CrIS
CARB emissions

## Slide 21: Final comments
CO from CrIS
  Will provide continuity to database established by AIRS, MOPITT and TES
  High resolution CrIS data is essential for accurate retrieval
  Algorithm to be delivered to the Sounder SIPS by the end of 2016
NH3 from CrIS
  Leverages experience with TES NH3
  Sensitive to only higher amounts (> 1.0 ppbv) of NH3
  Requires some thermal contrast to detect NH3
  Captures spatial variability as measured by a surface instrument
  Provides greater temporal and spatial coverage than aircraft campaigns or surface networks or even TES
  Algorithm to be delivered to the Sounder SIPS by the end of 2015

## Slide 22: Acknowledgements
  Markus Mueller and Tomas Mikoviny from the PTR instrument team
  PICARRO instrument team
  TES team at JPL
  Jesse Bash and Rober Pinder from the EPA
  Research was supported by
    the Jet Propulsion Laboratory, California Institute of Technology under contract to the National Aeronautics and Space Administration (NASA).
    NOAA Climate Program Office (CPO) Grant number NA130AR4310060
    CU support from NASA grant NNX10AG63G and EPA-STAR RD83455901
    Princeton support from NASA grant NNX12AN64H

## Slide 23: In situ and TES in North Carolina
NH3 vs time
NH3 vs source concentration
TES and surface measurements are qualitatively well correlated
Pinder et al., GRL, 2011

## Slide 24: Validation in North Carolina
North Carolina
Intense livestock farming (hogs, chickens, turkeys)
EPA CAMNet NH3 monitoring network
TES high spatial density observations (transects)
Feb – Dec 2009
Allows detection of spatial variability and seasonal trends
CHALLENGE
  TES: instantaneous profile over 5x8 km
  CAMNet: two week average at a surface point
  Cloudy summers!

## Slide 25: Eastern China: 2007-2009
Surface NH3
TES NH3 over Beijing
TES transect path
Beijing
Beijing
Shangdianzi
Meng et al., ACP, 2011
Shangdianzi

## Slide 26: South Asia: July-August 2007
Indus River Valley
High NH3 north of New Delhi and in the northern Indus valley

## Slide 27: Global NH3 results
Seasonal TES NH3 means from 2009 Global Surveys
High NH3 in North American growing season
Hotspot over India and elevated amounts over eastern China
Biomass burning signal over South America and Africa

## Slide 28: Measuring NH3 daily variations
North Carolina in situ data
CMAQ model with different temporal emission profiles
  Static profile
  Dynamic profile

## Slide 29: NH3 from a geostationary platform
CMAQ vs Simulated Retrievals
TES-like instument
Geostationary platform
Provides data every three hours
CMAQ profiles over California for a warm July day
Difference in CMAQ NH3 matches difference in retrieved NH3

## Slide 30: TES NH3 and CO
Monthly NH3 RVMR
July 2010
Aug 2010
Sept 2010
Monthly CO at 681 hPa
NH3 from TES V005 operational product
Biomass burning in South America is evident in both CO and NH3 maps
High NH3 values over northern India

## Slide 31: And now …
NH3
Shephard et al.[2011]