## Slide 1: VIIRS Low Light Imaging Applications
Christopher D. Elvidge, Ph.D.
Earth Observation Group
NOAA National Geophysical Data Center
Boulder, Colorado USA
chris.elvidge@noaa.gov
Kimberly Baugh, Feng-Chi Hsu, Mikhail Zhizhin, Tilottama Ghosh
Cooperative Institute for Research in the Environmental Sciences
University of Colorado
November 21, 2014

## Slide 2
Cities and human
settlements
Industrial Sites
Boats
Gas Flares
Fires
Lights
At
Night!

## Slide 3: VIIRS Low Light Imaging
Signal intensification to detect faint radiant emissions – the DNB.
Collection of daytime channels at night to detect radiant emissions that are obscured by reflected sunlight.

## Slide 4: VIIRS Provides Improved Spatial Resolution Fishing Boat Detections
VIIRS October 15, 2012 01:30
DMSP-OLS October 14, 2012 19:30

## Slide 5: What Makes VIIRS Better Than DMSP?
The VIIRS DNB footprint is 45 times smaller than the DMSP pixel footprint!
VIIRS Day / Night Band
742 m2 footprint
DMSP OLS
5 km2 footprint

## Slide 6: What Else Makes VIIRS Better Than DMSP?
Quantization: VIIRS 14 bit versus 6 bit for DMSP.
Dynamic Range: Due to limited dynamic range, DMSP data saturate on bright lights in operational data collections.
Lower Detection Limits: VIIRS can detect dimmer lighting than DMSP.
Quantitative: VIIRS is well calibrated, the DMSP visible band has no in-flight calibration.
Multispectral: VIIRS has additional spectral bands to discriminate combustion sources from lights and to characterize the optical thickness of clouds.

## Slide 7: Current Status of NGDC DNB Products
Nightly mosaics in png and Google Earth Super-overlay formats http://ngdc.noaa.gov/eog/viirs/download_ut_mos.html
Rough monthly averages. Four preliminary products are available at: http://ngdc.noaa.gov/eog/viirs/download_monthly.html
Monthly and annual cleaned nighttime lights still in development
  With stray light correction
  Free of solar, lunar, aurora, South Atlantic Anomaly detector hits
  Filtered to remove lightning
  Combustion sources removed
  Background noise removed

## Slide 8
Average VIIRS DNB Composite - January 2013 Contrast Enhanced to Show the Flaws
Dimensions 86400 x 33601. Too large to output as GEOTIFF!
Original units multiplied by a billion (E9) to yield nanoWatts/(cm2.sr)
NGDC is working on algorithms to make research quality nighttime lights: removal of background noise, aurora, ionospheric detector hits, lightning, fires, fuzzy lights.
Aurora
Sunlit

## Slide 9: Color composite of three monthly average DNB products. 201204 = blue 201301 = green 201405 = red Blue indicates power outages in 2013 and 2014. Purple indicates power outage in 2013.
Syria
Nighttime lights should be used cautiously in LCLUC
analyses due to their plasticity

## Slide 10: Color composite of three monthly average DNB products. 201204 = blue, 201301 = green, 201405 = red
Syria
Red lines on Turkish side of border.
Refugee camps? 24 hour border control operation?

## Slide 11: VIIRS DNB Boat Detection System (Prototype)
An automatic system to report the date, time, location and radiance of boat detections.
Output as csv and kmz.
Kml provides a semi-transparent contrast enhanced DNB image
Prototyping is being done in Indonesia, sponsored by USAID.
Customer is the Indonesia Ministry of Marine Affairs and Fisheries.
System works well when moonlight is low.
Second round of development will focus on high lunar conditions.
Analog to fire detection products.
http://www.ngdc.noaa.gov/eog/viirs/download_indo_boat.html

## Slide 12: Boat Detection Flow Chart

## Slide 13: Sharpness Index Cuong T. Vu and Damon M. Chandler, "S3 A Spectral and Spatial Measure of Local Perceived Sharpness in Natural Images", IEEE Transaction on Image Processing, 21 (3), September 2011.

## Slide 14: Lightning Detection

## Slide 15: DNB Spike Detector
DNB
DNB minus despiked
With background suppressed a threshold is used to detect the spikes
Median
Filtered
DNB
(despiked)

## Slide 16: Transect Across Boat Cluster

## Slide 17: Transect Across Boat Cluster

## Slide 18: Remove detections on land

## Slide 19: Boat Detections Running for Indonesia DNB as semi-transparent overlay

## Slide 20: Boat Detections Running for Indonesia

## Slide 21
M11
Approved
VIIRS Nightfire (VNF): A global multispectral fire product
Nine channels of data are collected at night
Nighttime collection of channel 11 is expected to start in 2015

## Slide 22: Gas flares are readily detected in the VIIRS M10 spectral band

## Slide 23: Detection Limits At 1800 K flares as small as 0.25 m2 are detectable
M10
M13
Flares
Gas Flares
Biomass
Burning

## Slide 24: Bakken Oil Field DNB March 10, 2013

## Slide 25: Overlay M10 as red. 352 lights. 104 flares. 29.5%!

## Slide 26: Why Multispectral?
To get at the Planck curves!
Daily files are in csv and kmz formats

## Slide 27: Typical Biomass Burning Detection
Lower temperature than gas flaring.
Often these have larger source size than gas flares.
North Dakota

## Slide 28: Daily VNF data are available at: http://ngdc.noaa.gov/eog/viirs/download_viirs_fire.html
Current processing typically runs with a four hour delay

## Slide 29: Applications for VNF data
NGDC uses the data map and track gas flaring worldwide.
Estimation of carbon and Nox emissions from gas flaring.
Prospecting favorable sites for natural gas recovery.
VNF temperatures and source sizes may be useful in modeling fire induced land cover change.
As an indicator of encroachment into protected and high biodiversity value areas.

## Slide 30: EOG Publications
VIIRS Nightfire: Satellite pyrometry at night http://www.mdpi.com/2072-4292/5/9/4423
What is so great about nighttime VIIRS data for the detection and characterization of combustion sources? http://dx.doi.org/10.7125/APAN.35.5
Using the short-wave infrared for nocturnal detection of combustion sources in VIIRS data. http://dx.doi.org/10.7125/APAN.35.6
Why VIIRS data are superior to DMSP for mapping nighttime lights. http://dx.doi.org/10.7125/APAN.35.7
Nighttime lights compositing using the VIIRS day-night band: Preliminary results . http://dx.doi.org/10.7125/APAN.35.8
Illuminating the capabilities of the Suomi NPP VIIRS
Day/Night Band. http://dx.doi.org/10.3390/rs5126717