## Slide 1: Applications of the Land Information System (LIS)
Fifth Meeting of the Science Advisory Committee
18-20 November, 2009
Jonathan Case
transitioning unique NASA data and research technologies to operations
National Space Science and Technology Center, Huntsville, AL

## Slide 2: LIS: Relevance to NASA/SPoRT
transitioning unique NASA data and research technologies to operations
NASA asset developed by GSFC
LIS benefit to SPoRT end-users
  LSM fields for model initialization
  Diagnostics for short-term forecasts of temperatures and/or convective initiation
LIS framework is capable of incorporating NASA EOS datasets
  MODIS-derived land cover
  Assimilation of AMSR-E soil moisture

## Slide 3: Accomplishments since 2007 SAC Meeting
transitioning unique NASA data and research technologies to operations
2007 SAC Recommendations: “…look at some non-quiescent cases….Move toward a systematic evaluation with satellite and radar”
Verification study of daily WRF runs from summer 2008: Focus on precipitation
Configured real-time 3-km LIS
  Hourly output
  Used to initialize NWS Miami WRF runs
Publications and presentations
  J. Hydrometeor. (2008)
  Annual AMS meetings (2008, 2009)
  WRF Users Workshops (2008, 2009)

## Slide 4: High-Level Overview of LIS
transitioning unique NASA data and research technologies to operations
LSM First Guess / Initial Conditions
WRF
Land Surface Models (LSMs) Noah,VIC, SIB, SHEELS
Coupled or
Forecast Mode
Uncoupled or
Analysis Mode
Global, Regional
Forecasts and
(Re-) Analyses
Station Data
Satellite Products
ESMF
Data Assimilation
(v, LST, snow)

## Slide 5: Approach and Methods
transitioning unique NASA data and research technologies to operations
Daily 27-h WRF simulations over SE U.S.
  4-km grid spacing, 03z initializations
  81 total forecasts from Jun – Aug 2008
  Control: Initial / boundary conditions from NCEP 12-km NAM model
  Experiment: LIS LSM and MODIS SST initialization data (LISMOD)
Evaluation and Verification
  Focus on (convective) precipitation verification
  Meteorological Evaluation Tools (MET)
  Method for Object-Based Diagnostic Evaluation (MODE)
Case studies of severe convection with GSFC/NSSL
ny = 311
nx = 309

## Slide 6: LIS Spin-up Run and WRF Initialization
transitioning unique NASA data and research technologies to operations
Run LIS/Noah offline from Jan 2004 to Sep 2008
  Same soil and vegetation parameters as in WRF
  Same horizontal resolution, but different grid
    Simulates a realistic real-time setup
  Atmospheric forcing used to drive LIS/Noah:
    3-hourly Global Data Assimilation System analyses
    Hourly Stage IV radar + gauge precipitation
  Run long enough for soil to reach equilibrium state
Initialize WRF land surface with LIS output and MODIS SSTs

## Slide 7: Validation Against SCAN Soil Moisture Obs
transitioning unique NASA data and research technologies to operations
LIS (solid lines w/ labels) consistently drier than Control/NAM
  Reduced moist bias in top model layer (blue)
  Reduced RMSE in top 2 model layers (red)
  Increased dry bias in lower layer (green)
Apples vs. Oranges comparison (obs level vs. model layer)

## Slide 8: 10 Jun 2008 Sensitivity Example 0-10 cm soil moisture SST Differences
transitioning unique NASA data and research technologies to operations

## Slide 9: 10 Jun 2008: 1224 hour forecasts Sensible Heat Flux 1-hour Precipitation
transitioning unique NASA data and research technologies to operations
CNTL
LISMOD
DIFF
Stage IV

## Slide 10: 1-h Traditional Precip Verification (1224 hours; JunAug 2008)
WRF has an overall high bias
LISMOD reduces bias, esp. mid-AM to early-PM (1218 h; 1521z)
WRF generally has low skill (right)
LISMOD incrementally improves skill

## Slide 11: Traditional Precip Verification Problem [from Baldwin et al. (2001), NWP/WAF conf.]
transitioning unique NASA data and research technologies to operations
Both forecasts have same bias
Using traditional measures, forecast #2 has larger RMS error & lower threat score
Which forecast is “better”?
Need non-standard verification method!
obs
Fcst #1
Fcst #2

## Slide 12: MET/MODE Object Verification
transitioning unique NASA data and research technologies to operations
Obs Precip
Fcst Precip
 80 km
Precipitation “objects” identified based on several spatial attributes
Forecast objects matched to obs objects (i.e. “hit”) based on
  Distance between objects
  Similarities in spatial attributes
In our use of MODE, fcst object must be within 80 km of obs object
  Ensures that convection on Florida’s West Coast does not get matched with convection on East Coast

## Slide 13: 10 Jun: MODE 10-mm/(1 h) Precip Objects
transitioning unique NASA data and research technologies to operations
Control
LISMOD
Matched
Forecast
Objects
(“hits”)
Matched
Observed
Objects

## Slide 14: 10 Jun: MODE 10-mm/(1 h) Precip Objects
transitioning unique NASA data and research technologies to operations
Control
LISMOD
Un-matched
Forecast
Objects
(false alarms)
Un-matched
Observed
Objects
(misses)

## Slide 15: 10 Jun: MODE 10-mm/(1 h) Precip Objects
transitioning unique NASA data and research technologies to operations
 | Control |  | LISMOD | 
Fcst hour | Grid Area Match | Grid Area Un-match | Grid Area Match | Grid Area Un-match
12 | 0 | 115 | 0 | 115
13 | 0 | 93 | 0 | 64
14 | 0 | 222 | 0 | 108
15 | 0 | 492 | 0 | 474
16 | 0 | 802 | 232 | 587
17 | 388 | 544 | 606 | 653
18 | 419 | 1039 | 470 | 711
19 | 108 | 1122 | 186 | 916
20 | 318 | 680 | 271 | 674
21 | 394 | 301 | 382 | 646
22 | 0 | 596 | 110 | 424
23 | 28 | 632 | 30 | 501
24 | 0 | 328 | 0 | 417
Control
LISMOD

## Slide 16: MODE 1-h Precip Object Verification: (Un-)Matched Differences by Model Run, 1224 h Forecasts
transitioning unique NASA data and research technologies to operations
Quantity | # Forecasts Improved | # Forecasts Degraded
5-mm matched | 39 | 41
5-mm unmatched | 56 | 25
10-mm matched | 37 | 39
10-mm unmatched | 48 | 33
25-mm matched | 13 | 8
25-mm unmatched | 46 | 32
Quantity (mean # grid points per model run) | Control | LISMOD | Difference (LISMOD – Control) | % Change
5-mm Matched | 11,911 | 12,045 | 134 | 1.1%
5-mm Unmatched | 17,750 | 17,175 | -575 | -3.2%
10-mm Matched | 2,456 | 2,562 | 106 | 4.3%
10-mm Unmatched | 6,798 | 6,538 | -260 | -3.8%
25-mm Matched | 60 | 60 | 0 | 0%
25-mm Unmatched | 549 | 505 | -44 | -8.0%

## Slide 17: Case Studies of Severe Convection
transitioning unique NASA data and research technologies to operations
CNTRL
NASA/
LIS
NASA/LIS:
More robust convection in TX Panhandle
WRF runs using NASA assets
  28 March 2007 tornado outbreak
  LIS + Goddard radiation physics improved convective forecasts
  Additional cases to be run using NSSL/WRF operational domain
NASA Unified WRF, coupling of:
  Satellite data simulator unit
  Land Information System
  NASA/Goddard physics in WRF
  Atmos. chemistry (GO-CART)
  NASA GEOS-5 global model

## Slide 18: Real-time LIS/Noah at SPoRT
transitioning unique NASA data and research technologies to operations
3-km LIS over southeast U.S.
  Spin-up run; restarts 4x per day
  Hourly output posted to ftp site
LIS option in WRF Environmental Modeling System (EMS), v3
  LIS initializations at NWS Miami, FL
LIS output for diagnostics
  Readily displayable in AWIPS II
  NWS BHM: Convective initiation
  Other short-term forecasting issues (low temps, fire weather, etc.)

## Slide 19: Summary and Conclusions
transitioning unique NASA data and research technologies to operations
Simulation methodology using NASA data and tools
  LIS land surface + MODIS SST composites
  High-resolution representation of land/water surface, consistent with local & regional model resolution
  Precipitation verification using object matching techniques in MET
  Improvements to 1-hour daytime precipitation
  Decrease in over-prediction of precipitation
    Likely related to overall drier LIS soil moisture
Implemented real-time LIS runs at SPoRT
  Initialize LSM fields in WRF EMS
  Possible diagnostics for short-term forecasting

## Slide 20: Future Work
transitioning unique NASA data and research technologies to operations
Submit SE U.S. verification study to Wea. Forecasting
Incorporate MODIS vegetation fraction
  Test in offline LIS and LIS/WRF coupled runs
Explore diagnostic utility of real-time LIS
  Collaboration with NWS Birmingham, AL
  Extend Koch and Ray (1997) convergence zones study to include LSM boundaries
Support NWS offices using real-time LIS
  WRF EMS model initialization
  Ingest into AWIPS II for diagnostics

## Slide 21: Backup Slides
transitioning unique NASA data and research technologies to operations

## Slide 22: Validation Against SCAN Soil Temperatures
transitioning unique NASA data and research technologies to operations

## Slide 23: Obligatory Point Verification
transitioning unique NASA data and research technologies to operations
LISMOD is slightly warmer/drier than the Control during the day
Marginally larger RMSE
Little to no differences in wind errors and MSLP (not shown)
2-m/10-m Bias
2-m/10-m RMSE

## Slide 24: 3-h Traditional Precip Verification: (327 hours; Jun-Aug 2008)
WRF has an overall high bias
LISMOD reduces bias some, esp. during day- light hours (12-24 h)
WRF generally has low skill (Heidke SS, right)
LISMOD incrementally improves skill

## Slide 25: MODE 1-h Precip Object Verification: Area Matched vs. Area Un-matched: All forecasts
transitioning unique NASA data and research technologies to operations